## Slide 1
Sanjivani College of Engineering, Kopargaon
(An Autonomous Institute, Affiliated to SPPU, Pune)
Department of Computer Engineering, NBA Tier-1 Accredited
Computer Networks CIA Activity Presentation
T.Y. B.Tech – Computer Engineering | AY 2026–2027 | Div-[ A]
Project Title
Adaptive Error Correction for High-Noise Wireless Communication
Submitted By
Deokar Sai | Palande Siddharth | Deokar Aditya | Chavan Aniket
Under the Guidance of
Dr. P. N. Kalavadekar
Associate Professor
Notes: Introduce the team, the course (Computer Networks) and the project topic: an adaptive error-correction system that changes its coding strength with channel quality.

## Slide 2: Introduction
“Use strong protection when the channel is poor, and save bandwidth when it is good.”
Wireless channels suffer noise, interference and fading, which flip bits from 0 to 1 or 1 to 0.
Error-control coding adds controlled redundancy so the receiver can detect or correct errors.
A fixed code wastes bandwidth on good channels and may be too weak on bad ones.
Our project is a simulation that selects the coding level from SNR and reports BER, throughput and redundancy.
Noisy wireless link
Transmitter
1 0 1 1 0 1 0
Noisy channel
Noise • Interference
Attenuation • Fading
Receiver
1 1 1 1 0 0 0
Flipped bits = transmission errors
Notes: Wireless links flip bits. Error-control coding adds redundancy so the receiver can fix them, but strong coding wastes bandwidth when the channel is good. This project chooses the coding strength from the SNR.

## Slide 3: Problem Definition
Problem: Develop a simulation-based wireless system that selects the error-correction strength according to channel conditions, balancing data reliability and transmission efficiency.
INPUT
Data and channel quality
Random binary data (10,000 bits)
SNR value from 0 to 12 dB
Noise (bit-flip) probability
PROCESS
Adaptive coding and decoding
Select coding level from SNR
Encode and send through noisy channel
Decode at the receiver
OUTPUT
Performance results
Bit Error Rate and error count
Effective throughput
Redundancy factor
Notes: The system takes random data and an SNR value, chooses a coding level, sends the coded bits through a simulated noisy channel and reports the results.

## Slide 4: Objectives
1
Study the effect of noise on wireless binary data transmission
2
Simulate a noisy wireless communication channel
3
Implement Hamming (7,4) and triple repetition coding
4
Design an SNR-based adaptive controller
5
Select the error-correction level dynamically
6
Calculate BER, throughput and redundancy
7
Compare adaptive coding with fixed Hamming (7,4)
8
Analyse the reliability–efficiency trade-off
Notes: Eight objectives: from studying the effect of noise to analysing the reliability and efficiency trade-off.

## Slide 5: Theoretical Background
Error Control Approaches
Type | Idea | Drawback
FEC | Add redundancy; receiver corrects errors | Extra bits sent
ARQ | Detect errors; request retransmission | Delay and extra traffic
This project focuses on FEC (highlighted).
Why adaptive coding?
Good channel: strong coding only adds overhead
Poor channel: weak coding leaves many errors
Matching coding to SNR balances both
Hamming (7,4) Code
n = 7, k = 4, rate = 4/7 ≈ 0.571
4 data bits become 7 coded bits
Parity bits found by XOR
Syndrome gives the error position
Corrects a single-bit error per block
Triple Repetition
0 → 000 1 → 111
Each coded bit is sent three times
Receiver uses majority voting
Tolerates one flipped bit in three
Notes: FEC corrects errors at the receiver without retransmission and is the approach used here. Hamming (7,4) corrects one error per block; triple repetition uses majority voting.

## Slide 6: Literature Survey and Research Gap
Code | Key Feature | Complexity | In this project
Hamming (7,4) | Corrects a single-bit error per block | Low | Implemented
Triple repetition | Majority voting over three copies | Low | Implemented
LDPC | Sparse parity-check codes; 5G NR data channels | High | Studied only
Polar | Channel polarisation; 5G NR control channels | High | Studied only
Research Gap
Strong codes are costly to implement in a small educational project. A simple, understandable simulation showing how coding strength follows channel quality is needed.
Our Contribution
Not a new code. Existing codes are used as building blocks, and the work focuses on the adaptive selection of coding strength using SNR.
Notes: Advanced codes like LDPC and Polar are used in 5G NR but are complex. This project uses simple established codes and focuses on the adaptive controller.

## Slide 7: Proposed System
Generate 10,000 bits
Select coding level (SNR)
Encode data
Transmit through noisy channel
Decode and measure
More SNR values?
yes
no
Store results and compare
1
Data Generation
10,000 random bits for every SNR value.
2
Adaptive Controller
Chooses Level 1, 2 or 3 from the SNR.
3
Encoding
Applies no coding, Hamming or Hamming + repetition.
4
Noisy Channel
Flips bits with a probability set by the SNR.
5
Decoding
Majority vote and Hamming decoding recover the data.
6
Performance Analysis
BER, throughput and redundancy; compared with fixed Hamming.
Notes: Walk through the flowchart from top to bottom. The loop repeats until every SNR value has been simulated.

## Slide 8: System Architecture
Random Data Generator
Adaptive Controller (SNR)
Level 1 / Level 2 / Level 3 Encoder
Noisy Channel
Adaptive Decoder
Performance Analysis
BER / Throughput / Redundancy
Data Generator
Creates 10,000 random bits (0s and 1s) per run.
Adaptive Controller
Picks the level using thresholds of 4 dB and 8 dB.
Encoder
No coding, Hamming (7,4), or Hamming plus triple repetition.
Noisy Channel
Random bit flips; lower SNR gives higher flip probability.
Decoder
Majority vote, then Hamming decode, depending on level.
Performance Module
BER, throughput, redundancy, error count; CSV output.
Notes: Seven stages from data generation to performance analysis. The controller is the only adaptive block.

## Slide 9: Adaptive Coding Levels
Level | Coding Method | SNR Condition | Protection | Redundancy
Level 1 | No error correction | SNR ≥ 8 dB | Low | 1.00
Level 2 | Hamming (7,4) | 4 ≤ SNR < 8 dB | Medium | 1.75 (7/4)
Level 3 | Hamming (7,4) + triple repetition | SNR < 4 dB | High | 5.25 (7/4 × 3)
Decision rule
if SNR >= 8 dB -> Level 1
else if SNR >= 4 dB -> Level 2
else -> Level 3
Thresholds are predefined and fixed.
Guiding principle
Poor channel → strong protection → high redundancy → lower efficiency.
Good channel → little or no protection → low redundancy → higher efficiency.
Notes: The controller follows one rule: stronger protection when the channel is poor, less redundancy when it is good. Redundancy is 1.00, 1.75 and 5.25 for the three levels.

## Slide 10: Algorithm
Adaptive error correction
1
Generate 10,000 random bits
2
Compute noise probability from the SNR
3
Select Level 1, 2 or 3 using the thresholds
4
Encode, pass through the noisy channel, decode
5
Calculate BER, throughput and redundancy
6
Repeat for all SNRs, then run fixed Hamming and compare
Pseudocode
for SNR in 0, 2, 4, ... 12:
data = generate(10000)
p = noiseProb(SNR)
level = selectLevel(SNR)
coded = encode(data, level)
rx = noisyChannel(coded, p)
out = decode(rx, level)
BER = errors(data, out) / 10000
store(BER, throughput, redundancy)
repeat with fixed Hamming (7,4)
compare adaptive and fixed
Notes: One simulation run per SNR value; the same experiment is then repeated with fixed Hamming (7,4) for comparison.

## Slide 11: Coding Working Example
Hamming (7,4) bit positions
P1
1
P2
2
D1
3
P4
4
D2
5
D3
6
D4
7
Parity bits (P) are computed with XOR
Receiver calculates syndrome bits
Syndrome value 1–7 is the error position; that bit is flipped back
Level 3 pipeline
Data
Hamming
× 3
Channel
Vote
Hamming
Encode → send → decode
Majority voting (triple repetition)
Received | Decoded bit
000 | 0
001 | 0
010 | 0
011 | 1
100 | 0
101 | 1
110 | 1
111 | 1
The output equals the bit that appears at least twice.
Notes: Hamming places parity bits at positions 1, 2 and 4. For Level 3 every Hamming bit is also tripled, and the receiver first takes a majority vote.

## Slide 12: Experimental Results
SNR (dB) | Adaptive |  |  |  | Fixed Hamming (7,4) | 
 | Level | BER | Throughput % | Redundancy | BER | Throughput %
0 | Level 3 | 0.5045 | 9.44 | 5.25 | 0.5006 | 28.54
2 | Level 3 | 0.2474 | 14.34 | 5.25 | 0.3464 | 37.35
4 | Level 2 | 0.2064 | 45.35 | 1.75 | 0.1957 | 45.96
6 | Level 2 | 0.0991 | 51.48 | 1.75 | 0.0955 | 51.69
8 | Level 1 | 0.0773 | 92.27 | 1.00 | 0.0481 | 54.39
10 | Level 1 | 0.0472 | 95.28 | 1.00 | 0.0210 | 55.94
12 | Level 1 | 0.0326 | 96.74 | 1.00 | 0.0073 | 56.73
Level 1 = no coding, Level 2 = Hamming (7,4), Level 3 = Hamming + triple repetition. Fixed redundancy is always 1.75.
Observation: redundancy drops from 5.25 to 1.00 as SNR rises, and adaptive throughput reaches 96.74% at 12 dB.
Notes: 10,000 bits per SNR value, SNR from 0 to 12 dB. The adaptive system switches levels at 4 dB and 8 dB. Results come from adaptive_results.csv and fixed_results.csv.

## Slide 13: Result Analysis
Chart: BER vs SNR
| 0 | 2 | 4 | 6 | 8 | 10 | 12
Adaptive | 0.5045 | 0.2474 | 0.2064 | 0.0991 | 0.0773 | 0.0472 | 0.0326
Fixed Hamming | 0.5006 | 0.3464 | 0.1957 | 0.0955 | 0.0481 | 0.021 | 0.0073
Chart: Throughput (%) vs SNR
| 0 | 2 | 4 | 6 | 8 | 10 | 12
Adaptive | 9.44 | 14.34 | 45.35 | 51.48 | 92.27 | 95.28 | 96.74
Fixed Hamming | 28.54 | 37.35 | 45.96 | 51.69 | 54.39 | 55.94 | 56.73
Adaptive BER is higher at 8 to 12 dB because coding is switched off.
Adaptive throughput gain comes from removing coding overhead.
Notes: BER falls as SNR rises for both systems. Adaptive throughput jumps when the controller switches to Level 1 at 8 dB, while fixed Hamming stays near 55%.

## Slide 14: Adaptive vs Fixed Coding
Chart: Adaptive redundancy factor vs SNR (dB)
| 0 | 2 | 4 | 6 | 8 | 10 | 12
Adaptive redundancy | 5.25 | 5.25 | 1.75 | 1.75 | 1 | 1 | 1
Results at 12 dB
Adaptive
0.0326
BER
96.74%
Throughput
1.00
Redundancy
Fixed Hamming
0.0073
BER
56.73%
Throughput
1.75
Redundancy
Fixed Hamming gives lower BER, but sends more bits. Adaptive coding gives a better balance of reliability and efficiency.
Notes: At 12 dB the adaptive system trades some reliability for much higher efficiency. The redundancy chart shows the three levels used across the SNR range.

## Slide 15: Key Features and Limitations
✓
Key Features
SNR-based automatic selection of 3 coding levels
Hamming (7,4) and triple repetition implemented
Measures BER, throughput, redundancy and errors
Compared with a fixed Hamming system
CSV output for graphs and analysis
Platform-independent Java program
!
Limitations
Software simulation; no RF hardware
Simplified bit-flip channel, not AWGN/BPSK
Fixed, predefined SNR thresholds
LDPC and Polar codes not implemented
No real-time channel estimation
No fading, Doppler or synchronisation effects
Notes: Be upfront about scope: this is a simulation with a simplified channel, not a physical-layer implementation.

## Slide 16: Future Scope and Applications
Future Scope
1
Real-time channel estimation using pilot symbols
2
AWGN, Rayleigh and Rician fading channels
3
LDPC and Polar codes as extra coding options
4
Machine learning to predict the best coding level
5
Real hardware: ESP32, SDR, Wi-Fi or LoRa modules
6
More metrics: latency, energy, packet loss
Applications
Wireless sensor networks
IoT communication
Mobile communication
Wi-Fi communication
Satellite communication
Notes: The concept applies wherever channel quality changes. Future work makes the channel and the controller more realistic.

## Slide 17: Conclusion
The Java simulation selects one of three coding levels from the SNR.
Stronger coding is used at low SNR; overhead is reduced at high SNR.
At 12 dB: 96.74% throughput and redundancy 1.00, against 56.73% and 1.75 for fixed Hamming.
Fixed Hamming gives lower BER at some high-SNR points but always carries overhead.
The project demonstrates the core idea of adaptive error-control coding for variable wireless channels.
96.74%
Throughput
adaptive at 12 dB (fixed: 56.73%)
1.00
Redundancy
adaptive at 12 dB (fixed: 1.75)
Notes: Close by linking back to the trade-off: coding strength should follow channel quality.

## Slide 18
Sanjivani College of Engineering, Kopargaon
(An Autonomous Institute, Affiliated to SPPU, Pune)
Department of Computer Engineering, NBA Tier-1 Accredited
Thank You
Questions?
Notes: Invite questions.